## Slide 1
Elmer FEM – Dakota interface
Anjali Sandip, Ph.D.
Senior Lecturer
Department of Mechanical Engineering
University of North Dakota
Notes: 1

## Slide 2
Cantilever beam - numerical model 1,2
Parameters:
L: length (m)
W: width (m)
T: thickness (m)
ρ: density (kg/m3)
E: Young’s modulus (N/m2)
X: horizontal load (N)
Y: vertical load (N)
Responses:
M: mass (kg)
S: stress (Pa)
D: displacement (m)
M = ρ × w ×t ×L
[1]. Bayoumi, S. (2018). Engineering solid mechanics: fundamentals and applications. Routledge.
[2]. Sandia Dakota (2015). Sandia Dakota training materials. Retrieved from https://dakota.sandia.gov/training/dakota-training-materials

## Slide 3
Cantilever beam – Finite element (FE) model in Elmer
Module 4 | 
Geometry | Rectangular block (L × w × t)
Mesh | Mesh element type – quadratic hexahedral elements Mesh size – 6073 nodes, 1200 elements
Simulation setup | Steady-state 3-dimensional Cartesian coordinates
Equation | Linear elasticity theory
Material | Steel 3 Density = 8000 kg/m3 Young’s modulus = 2.0e11 Pa
Loads and boundary conditions | Loads – pressure distributed uniformly over the cross-sectional area on the free end in the X and Y directions Boundary conditions – same as numerical model
[3]. MatWeb (1996 – 2019). Steel, General Properties. Retrieved from http://www.matweb.com/search/datasheet.aspx?bassnum=MS0001&ckck=1
PRE-PROCESSING
External package
Build 3D CAD + mesh
Build FE model
Elmer GUI
RUN
Elmer Solver
Build FEM solution
POST-PROCESSING
ParaView
View results

## Slide 4
Constrained optimization of cantilever beam
Problem statement: Minimize the mass of the cantilever beam by 10% subject to following constraints
- 0.01 m < Width < 0.1 m
- 0.01 m < thickness < 0.1 m
# Constrained optimization of cantilever beam
method
optpp_newton
variables
continuous_design 2
#design variables - width (m), thickness (m)
descriptors 'w' 't'
initial_point 0.05 0.05
upper_bounds 0.1 0.1
lower_bounds 0.01 0.01
#fixed parameters – length (m), young’s modulus (Pa), density (kg/m3), horizontal load (N), vertical load (N)
continuous_state 5
descriptors 'L' 'E' 'p' 'X' 'Y'
initial_state 0.127 2.0e11 8000 1560 2225
Dakota input file

## Slide 5
Constrained optimization of cantilever beam
Problem statement: Minimize the mass of the cantilever beam by 10% subject to following constraints
- displacement < 2.6e-5 m
- stress < 350 MPa (steel/yield stress)
# Constrained optimization of cantilever beam
responses
# simulation output – mass (kg), displacement (m), stress (Pa)
descriptors 'mass' 'displacement' 'stress'
#minimize mass
objective_functions 1
#upper bounds on displacement and stress
nonlinear_inequality_constraints 2
nonlinear_inequality_upper_bounds 2.6e-5 3.5e8
numerical_gradients
numerical_hessians
#uncomment for conmin_mfd, optpp_q_newton, optpp_fd_newton
#no_hessians
Dakota input file

## Slide 6
Constrained optimization method selection
Optimization method selection criteria –
Smooth
Local minima
Continuous variables
Bound constraints
Nonlinear inequality constraints
Selected method type = Gradient based local

## Slide 7
Model type | Method name | Width (m) | Thickness (m) | Mass (kg) | Displacement (m) | Stress (Pa) | Function evaluations (#)
Numerical model | conmin_mfd | 0.01 | 0.01 | 0.109 | 3.75e-04 | 1.02e+08 | 22
 | optpp_q_newton | 0.05 | 0.05 | 2.54 | 1.64e-05 | 2.13e+07 | 18
 | optpp_fd_newton | 0.05 | 0.05 | 2.54 | 1.64e-05 | 2.13e+07 | 28
 | optpp_newton | 0.05 | 0.05 | 2.53 | 1.64e-05 | 2.13e+07 | 48
FE model | conmin_mfd | 0.01 | 0.01 | 0.11 | 4.02e-04 | 1.50e+08 | 22
 | optpp_q_newton | 0.05 | 0.05 | 2.54 | 2.02e-05 | 2.50e+07 | 18
 | optpp_fd_newton | 0.05 | 0.05 | 2.54 | 2.02e-05 | 2.50e+07 | 28
 | optpp_newton | 0.05 | 0.05 | 2.53 | 2.025e-05 | 2.50e+07 | 48
Results: Gradient-based local methods

## Slide 8
Model type | Method name | Width (m) | Thickness (m) | Mass (kg) | Displacement (m) | Stress (Pa) | Function evaluations (#)
Numerical model | coliny_cobyla | 0.01 | 0.05 | 0.95 | 7.11e-05 | 3.65e+07 | 7
 | coliny_pattern_search | 0.01 | 0.01 | 0.10 | 4.09e-04 | 1.06e+08 | 93
 | coliny_solis_wets | 0.01 | 0.01 | 0.10 | 4.03e-04 | 1.06e+08 | 89
 | mesh_adaptive_search | 0.03 | 0.04 | 1.5 | 2.59e-05 | 2.69e+07 | 184
FE model | coliny_cobyla | 0.01 | 0.05 | 0.95 | 7.35e-05 | 3.99e+07 | 7
 | coliny_pattern_search | 0.01 | 0.01 | 0.10 | 4.37e-04 | 1.17e+08 | 74
 | coliny_solis_wets | 0.01 | 0.01 | 0.10 | 4.21e-04 | 1.11e+08 | 92
 | mesh_adaptive_search | 0.04 | 0.04 | 1.92 | 2.49e-05 | 2.79e+07 | 131
Results: Derivative-free local methods